;=======Listing1.asm===========10/31/03;;Written by Ted Salazar;;This program configures the MAX3100 for 8-N-1 at 230k Baud and;transmits "THE QUICK BROWM FOX JUMPS OVER THE LAZY DOG" in an;endless loop. The UART-to-USB IC will receive the transmitted;data from the MAX3100 serial UART and echo the data over;the universal serial bus (USB).;----------------------------------	list	p=16f84	radix	hex;----------------------------------;	memory mappc			equ     0x02porta			equ	0x05portb			equ	0x06r_wconf_hbyte		equ	0x0cr_wconf_lbyte		equ	0x0dr_rconf_hbyte		equ	0x0er_rconf_lbyte		equ	0x0fr_wdata_hbyte		equ	0x10r_wdata_lbyte		equ	0x11r_rdata_hbyte		equ	0x12r_rdata_lbyte		equ	0x13r_temp			equ	0x14ncount			equ	0x15xcount			equ	0x16kcount			equ	0x17mcount			equ	0x18dout			equ	0x19dout1			equ	0x1adout2			equ	0x1bdout3			equ	0x1cdout4			equ	0x1ddout5			equ	0x1edout6			equ	0x1fmuxcount		equ	0x1echarcount		equ	0x1f;----------------------------------------------;*****;Main;*****	org	0x000start	movlw	0x20	;RB7 RB6 RB5 RB4   RB3 RB2 RB1 RB0			; 0   0   1   0     0   0   0   0			;sclk cs\ dout din  ( outputs....)	tris	portb	;dout = RB5 =  an input			;all other ports b's are outputs	movlw	0x40	;0x40 to w	movwf	portb	;cs\=1 			;sclk=0			;din=0			;dout=input			;RB0-RB3 = 0	movlw	0x00	;0x00 to w	tris	porta	;RA4 thru RA0 are outputs	movlw	0x00	;0x00 to w	movwf	porta	;RA4 thru RA0 = 0		call 	delay200ms;------------------------------------------------;*********************;Write Configuration;*********************	bcf	portb,6		;cs\=0	movlw	0xc0		;0xc0 to w	movwf	r_wconf_hbyte	;w to register	movf 	r_wconf_hbyte,0	; to w	call  	spi_8bit_word	; call subroutine;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>	movf	dout		; to w	movwf	dout1		; dout to dout1	;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%	movlw	0x00		;0x00 to w	movwf	r_wconf_lbyte	;w to register	movf	r_wconf_lbyte,0	; to w	call 	spi_8bit_word	; call subroutine;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>	movf	dout		; to w	movwf	dout2		; dout to dout2	;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%	bsf	portb,6	;	;cs\=1;	call	delay200ms;************************;Read Configuration;************************	bcf	portb,6		;cs\=0	movlw	0x40		;0x40 to w	movwf	r_rconf_hbyte	;w to register	movf 	r_rconf_hbyte,0	; to w	call  	spi_8bit_word	; call subroutine;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>	movf	dout		; to w	movwf	dout3		; dout to dout3	;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%	movlw	0x00		;0x00 to w	movwf	r_rconf_lbyte	;w to register	movf	r_rconf_lbyte,0	; to w	call 	spi_8bit_word	; call subroutine;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>	movf	dout		; to w	movwf	dout4		; dout to dout4	;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%	bsf	portb,6		;cs\=1;	call	delay200ms;------------------------------------------------;------------------------------------------------;*********************;Write Data1;*********************circle2	nop	movlw	0x00		;0x00 to w	movwf	muxcount	;0x00 to muxcount	movlw	0x2c		;dec 44 to w	movwf	charcount	;dec 44 to wcircle1 nop		bcf	portb,6		;cs\=0	movlw	0x80		; to w	movwf	r_wdata_hbyte	;w to register	movf 	r_wdata_hbyte,0	; to w	call  	spi_8bit_word	; call subroutine;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>	movf	dout		; to w	movwf	dout5		; dout to dout5	;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%	movf	muxcount,0	; muxcount to w	call    mux		; get data to xmit				; data in w	movwf	r_wdata_lbyte	; w to register	movf	r_wdata_lbyte,0	; to w	call 	spi_8bit_word	; call subroutine;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>	movf	dout		; to w	movwf	dout6		; dout to dout6	;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%	bsf	portb,6	;	;cs\=1	call	delay200ms;------------------------------------------------;------------------------------------------------	incf 	muxcount,1	;increment muxcount				;result in muxcount	decfsz	charcount,1	;decrement charcount				;result in charcount	goto	circle1			goto 	circle2		;------------------------------------------------;The "spi_8bit_word" subroutine takes the contents of;the various _hbyte and _lbyte registers and shifts;them out through the SPI port. This subroutine is;generic and can be used for any SPI device that ;does not use the DOUT line.;************spi_8bit_word;************	movwf	r_temp	;r_temp = w	movlw	0x08  	;0x08 to w	movwf	ncount	;0x08 to ncountbtfline	btfsc	r_temp,7;test bit 7 of r_temp	;skip if clear	goto	spi_hi	;spi_low	rlf 	r_temp,f	nop	bsf	portb,7	;sclk=1	nop;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>	btfsc	portb,5	;test DOUT of UART	goto	dout_hi_spi_low	rlf	dout,f	bcf	dout,0;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%sclklw1	bcf	portb,7	;sclk=0	decfsz	ncount	goto	btflineout	returnspi_hi	rlf	r_temp,f	bsf	portb,4 ;Din=1	nop	bsf	portb,7	;sclk=1;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%; =>	btfsc	portb,5	;test DOUT of UART	goto	dout_hi_spi_hi	rlf	dout,f	bcf	dout,0;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%	nopsclklw2	bcf	portb,7	;sclk=0	bcf	portb,4	;Din=0	decfsz	ncount	goto	btfline	goto	out;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>dout_hi_spi_low	rlf	dout,f		bsf	dout,0		goto	sclklw1;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;=>dout_hi_spi_hi	rlf	dout,f		bsf	dout,0		goto	sclklw2;=>;%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%;-----------------------------------------------------;Delay Subroutine;xcount controls the delay time;i.e. xcount x 200ms = delay;********delay2sec;********	movlw	0x0A	;0x0A to w	movwf	xcount	;to xcountloadm	movlw	0xff	;0xff to w	movwf	mcount	;to mcountloadk	movlw	0xff	;0xff to w	movwf	kcount	;to kcountdeck	decfsz	kcount,f;dec k	goto	deck		decfsz	mcount,f;dec m	goto	loadk	;jump to loadk	decfsz	xcount,f;dec x	goto	loadm	;jump to loadm	return;-----------------------------------------------------;------------------------------------; mux subroutine; transmit data;*****mux;*****			addwf	pc,f	;add w to pc	retlw	0x54	;T	retlw	0x48	;H	retlw	0x45	;E	retlw	0x20	;"Space"	retlw 	0x51	;Q	retlw	0x55	;U	retlw	0x49	;I	retlw	0x43	;C	retlw	0x4b	;K	retlw	0x20	;"Space"	retlw	0x42	;B	retlw   0x52	;R	retlw	0x4f	;O	retlw 	0x57	;W	retlw	0x4e	;N	retlw 	0x20	;"Space"	retlw  	0x46	;F	retlw   0x4f	;O	retlw   0x58	;X	retlw	0x20	;"Space"	retlw	0x4a	;J	retlw	0x55	;U	retlw	0x4d	;M	retlw	0x50	;P	retlw	0x53	;S	retlw	0x20	;"Space"	retlw	0x4f	;O	retlw	0x56	;V	retlw	0x45	;E	retlw	0x52	;R	retlw	0x20	;"Space"	retlw	0x54	;T	retlw	0x48	;H	retlw	0x45	;E	retlw	0x20	;"Space"	retlw	0x4c	;L		retlw	0x41	;A	retlw	0x5a	;Z	retlw	0x59	;Y	retlw	0x20	;"Space"	retlw	0x44	;D	retlw	0x4f	;O	retlw	0x47	;G	retlw	0x20	;"Space";-----------------------------------------------------;-----------------------------------------------------;Delay Subroutine;xcount controls the delay time;i.e. xcount x 200ms = delay;********delay200ms;********	movlw	0x01	;0x01 to w	movwf	xcount	;to xcountloadm2	movlw	0xff	;0xff to w	movwf	mcount	;to mcountloadk2	movlw	0xff	;0xff to w	movwf	kcount	;to kcountdeck2	decfsz	kcount,f;dec k	goto	deck2		decfsz	mcount,f;dec m	goto	loadk2	;jump to loadk	decfsz	xcount,f;dec x	goto	loadm2	;jump to loadm	return;----------------------------------------;******	end;******;========================================; Blast time:;	memory unprotected;	watchdog timer disabled (default enabled);	standard crystal (4Mhz);	power-up timer on;========================================