Appendix A. Code Examples

Example Code for a Bounded Queue

### Variables and Constants

// These just make life easier

typedef unsigned char    u8;

typedef unsigned short   u16;

typedef unsigned int     u32;

typedef signed char      s8;

typedef short            s16;

typedef int              s32;

#define C_Q_MAX         (  8 )

#define C_Q_MAX_ID      ( C_Q_MAX * 2 )

#define C_Q_DATASIZE    (  7 )

#define C_Q_FULL        ( -1 )

#define C_Q_XSUM_ERROR  ( -2 )

#define C_FLASH_EMPTY   ( 0xFF )

// Size of this structure should be divisible by 4 for the

// code to work properly

typedef struct {

u16 iData[C_Q_DATASIZE];

u8 iID;

u8 iChecksum;

} QENTRY;

extern bool ChecksumValid(QENTRY *pEntry);

extern u16 dataFlashErasePage(void *pAddress);

extern u16 dataFlashWrite(void *pAddress, u16 iData);

extern QENTRY FlashQueue[C_Q_MAX]; // Mapped into Data Flash

extern u8 iQID;

extern u8 iQIndex;

### Initialization Code

/*

// queueInitialize()

//    This routine returns the current valid entry in the queue and

//    sets the global variable iQID to the ID of the current valid entry.

*/

short queueInitialize(void)

{

s16 iIndex;

iQID = 0;

// Find the last valid entry

for (iIndex=0;iIndex < C_Q_MAX-1; ++iIndex)

{

// If empty then return the previous entry

if (FlashQueue[iIndex].iID == C_FLASH_EMPTY)

{

iIndex = (iIndex + C_Q_MAX - 1) % C_Q_MAX;

iQID = FlashQueue[iIndex].iID % C_Q_MAX_ID;

return iIndex;

}

}

// Should never get here.  The queue is full, return error

return C_Q_FULL;

}

### Write Queue Entry Code

/*

// queueWriteEntry()

//    Writes new entry into the flash queue.

*/

short queueWriteEntry(QENTRY *pEntry)

{

void *pDest;

u8 i;

if (pEntry != NULL)

{

// Compute the new packet ID

iQID = (iQID + 1) % C_Q_MAX_ID;

// Compute the new Index

iQIndex = (iQIndex + 1) % C_Q_MAX;

// Set the packet ID

pEntry->iID = iQID;

// Calculate the checksum

pEntry->iChecksum = iQID;

for (i = 0; i < C_Q_DATASIZE; ++i)

pEntry->iChecksum += pEntry->iData[i];

// If next entry is full erase it.  There must always be at least

// one empty entry so the latest entry can be located.

if (FlashQueue[(iQIndex + 1) % C_Q_MAX].iID != C_FLASH_EMPTY)

{

// dataFlashErasePage erases two pages (2 words) at a time

// so we need to call it for every other word address in the entry.

for (i = 0; i < sizeof(QENTRY)/4; ++i)

dataFlashErasePage(((u16 *)&FlashQueue[(iQIndex + 1) % C_Q_MAX])

+ i*2);

}

// Write packet to flash

// Assumption is that entry will already be erased due to previous

// two lines of code.

pDest = &FlashQueue[iQIndex];

for (i = 0; i < sizeof(QENTRY)/2; ++i)

dataFlashWrite(pDest, ((u16 *)pEntry)[i]);

return true;

}

return false;

}